## Slide 1
逗猫机器人
Cat-Teasing Robot with LeKiwi Mobile Manipulator
[ Insert Image Here ]

## Slide 2
Sense – Plan – Act Loop
Perception
Detection
GroundingDINO / SAM
Localization
AprilTag pose estimation
Mapping
2D occupancy grid from RGB-D
Planning
Goal Position
Visibility-aware heuristic
Path Planning
A* on inflated grid
Motion Planning
Predefined arm pose library
Control
Base Control
Proportional velocity tracking
Arm Control
Joint position + wand swing
Safety Monitor
Distance-based emergency stop
← ─ ─ ─ ─ ─ ─ ─ ─ ─ ─ ─ FEEDBACK LOOP ─ ─ ─ ─ ─ ─ ─ ─ ─ ─ ─ →

## Slide 3
System Architecture & Implementation Status
Perception
Planning
Control
Hardware
Detection
Cat bbox GroundingDINO
READY
Localization
AprilTag 6-DoF pose
READY
Mapping
2D occupancy from depth
READY
Goal Selection
Partial-visibility heuristic
READY
Path Planning
A* + collision inflation
READY
Motion Plan
Pose library + wand trajectory
READY
Arm Control
Joint position command
READY
Base Control
Proportional velocity
READY
Actuators
LeKiwi servos + omni wheels
READY
Raspberry Pi
Onboard compute + camera
READY
Perception Integration
Camera → Detect → Localize → Map
Planning Integration
WorldState → Goal → Path → Arm Pose
Control Integration
Path → Velocity → Hardware
Hardware Integration
Pi → ZMQ → Actuators
End-to-End System Test: Fake Data Pipeline ✓ | Real Hardware TBD
MODULES
COMPONENTS
INTEGRATION